## Slide 1: Vehicle Vibration Analysis with C++
Courtney Armstrong
MEC 510, Final Project

## Slide 2: Outline
Motivation
Background
Problem Description
Code Structure
  Overview
  External Libraries
  Classes and Functions
Demonstration
Results

## Slide 3: Problem Background & Description

## Slide 4: Motivation
MATLAB can be used to successfully analyze a vehicle system
C++ analysis is much faster than MATLAB
  MATLAB must run on CPU, C++ can be run using GPU for complex calculations via CUDA
C++ also allows for direct comparison of multiple vehicle/road object combinations by simply defining more objects

## Slide 5: Vehicle Vibrations
Suspension systems in vehicles are designed to reduce uncomfortable motions felt by passengers while driving
  Utilizes springs and shock absorbers to control vibration transmitted through vehicle
Focused on reducing two kinds of motion
  Bounce (up and down motion)
  Pitch (front to back rotation)

## Slide 6: Vehicle Model
Bounce (x) and pitch (θ) are independent of one another
  Results in a two degree of freedom system with two coupled differential equations

## Slide 7: Vehicle Model
Mathematical equations governing bounce and pitch response derived from diagram
and are the forcing equations due to bumps on the road and vehicle speed

## Slide 8: Project Description
Understanding the vibration of the vehicle requires solving the equations of motion to determine x and θ
  Only x, θ, dx, dθ and t are variable (all other variables in equation are constants)
Using C++, along with external libraries, the equations can be solved based on user input of parameters

## Slide 9: C++ Code Structure

## Slide 10: Functionality Overview
User inputs car parameters or selects a vehicle class (based on SAE standards)
  Mass, damping, inertia, etc.
User inputs road parameters
  Wavelength, speed, and amplitude
User inputs analysis parameters
  Start time, end time, time step and initial values
Script outputs natural frequencies, mass and stiffness matrices and writes integration values to a text file

## Slide 11: External Libraries
Determining the solution for the coupled equations requires the use of linear algebra and differential equations
  Outside the scope of what MSVS libraries can do natively
Eigen
  High level, template library for matrix and vector linear algebra
Odeint
  High level, template library for solving differential equations
  Peer reviewed by Boost for accuracy
Notes: Go to code to explain classes!

## Slide 12: Vehicle Class
Stores all required constants for left hand side of motion equation (physical parameters of car)
Includes the functions required to determine:
  Natural frequency (Eigen)
Also includes functions to allow user to either define the vehicle parameters or pick pre-set parameters (SAE vehicle class)

## Slide 13: Road Class
Stores all required constants for forcing functions

## Slide 14: Verification

## Slide 15: Verification Setup
Vehicle Parameters
  Class 4 SAE Vehicle (Luxury vehicle, Jaguar XJ)
Road Parameters (moderately bumpy road)
  10 m/s velocity (approx. 22.4 mph)
  0.025 m peak amplitude (approx. 1”)
  0.5 m wavelength (approx. 20”)
Time period
  0-5 seconds

## Slide 16: MATLAB Results (ode45)

## Slide 17: C++ Results (Bulirsch–Stoer algorithm)
Chart: C++ Analysis - Response vs. Time

## Slide 18: Numerical Comparison
Percent Error
Error is within acceptable range, verification is successful!
Maximum Response Values |  | 
 | Bounce (m) | Pitch (rad)
C++ Analysis | 6.99x10-4 | 1.32x10-4
MATLAB Analysis | 6.86x10-4 | 1.39x10-4

## Slide 19: Questions?